## Slide 1: Mars: Science and Engineering (Week 2)
Howard Seltman
CMU Osher
Fall 2023

## Slide 2: Course Outline
Week 1
  Astronomy background
  Early flights with no or minimal success
  Mariner Program
Week 2
  1973: Soviet Mars program
  1975: US Viking program
  1990s: MGS, Pathfinder, Sojourner, Nozomi
Week 3
  Early 2000s: Odyssey, Spirit & Opportunity, Mars Express
  Late 2000s: Mars Reconnaissance Orbiter, Phoenix lander
Week 4
  2010s: Curiosity, MAVEN, Mangalayan, Insight
  2020s: Perseverance, Ingenuity, Tianwen, Emirati Hope
  Future: EscaPADE, Exo-Mars
  Far future: humans on Mars

## Slide 4: Pre-Viking Soviet Missions
Mars 4 to Mars 7 were intended for 1973 launch to pre-empt the 1976 US Viking missions, but planetary positioning was poor necessitating smaller payloads in the form of separate orbiter and lander launches
Mars 4 lander could not do course correction to due transistor failure but sent back 12 pictures at 1200 miles
Mars 5 orbiter developed an instrument compartment leak, so it operated in orbit for only 3 weeks and returned about 60 pictures and surface chemical composition data
Mars 6 lander returned data on a near-successful landing but crashed (or lost its radio)
Mars 7 lander failed to enter the Martian atmosphere and remained in heliocentric orbit

## Slide 5: Early US Landers
JPL’s Surveyors 1, 3, and 5-7 soft-landed on the moon starting in 1966

## Slide 6: The Cancelled “Voyager Mars” Program
“Voyager Mars” was part of the Apollo Applications Program
Planning was in 1966-1968 for 1974 launch with manned missions planned for the 1980s!
Based on Apollo spaceships, but later dismissed based on Mariner data on the Martian atmosphere
First major NASA program cancelled by Congress
Evolved into Viking 1 and 2
(Mariner 11 and 12 were sent to the outer planets and beyond, renamed as Voyager 1 and 2)

## Slide 7: Viking Mission Overview
Viking 1 and 2 each comprised an orbiter and a lander to reach Mars in 1976
Cost $1 billion ($5 billion in current value)
Search for life was a major goal
Over 20% of the cost relates to sterilization

## Slide 8: Viking Spacecraft

## Slide 9: Viking Engineering
5115-pound orbiters, 8 feet in diameter, powered by four 32-foot solar panels (620 watts), similar to the Mariners
Entry, Descent and Landing were the biggest unknowns
  Earth landings are based on aerobraking, sub-sonic parachutes, and a water landing (US) or retrorockets (USSR)
  Without an atmosphere, moon landings are based on retrorockets (and the lander need not be aerodynamic)
  On Mars the atmosphere is thin, but significant
  The strategy was aerobraking, hypersonic parachutes, and then retrorockets
1270-pound lander made of aluminum and titanium included RTG power source (60 watts from plutonium-236), twin 18K RAM onboard computers, weather station, seismometer, S-band radio with high and low gain antennas, UHF radio, 2 cameras, surface sampler boom, biology processor, descent engine and propellant tank. Similar to the Surveyors.

## Slide 10: Contemporaneous Viking Video
Viking Documentary (12:08) [garbled start, some bad subtitles]

## Slide 11: Orbiter Instrumentation
Twin 88-pound television cameras with telescopes and mechanical shutters and 160-megabyte tape recorders
  1056 lines by 1182 samples at 7 bits (128 intensity levels)
  1 megabyte per picture
  Six color filters: blue (0.35 to 0.53 µm), yellow (0.48 - 0.70), violet (0.35 - 0.47), green (0.50 - 0.60), red (0.55 - 0.70), and clear
  Each pixel is about 120 feet on a side at 900 miles elevation
Infrared spectrometer for water vapor mapping
Infrared radiometer for thermal mapping

## Slide 12: Lander Imager Engineering
Used cutting edge “facsimile” technology that had few moving parts and good balance of reliability and image quality for a reasonable (high) price and weight (16 pounds each)
Image rate is 4.7 lines per second
Could be baked to 110◦ C, and could transmit in real time (no storage) at 16K and 250 bits per second

## Slide 13: Lander Instrumentation
Gas chromatograph mass spectrometer for organic chemistry analysis of soil
  GC separates a mixture of volatile substances based on general chemical and/or physical properties
  MS creates ions and fragment ions and measures mass to charge ratio: fingerprints of specific organic chemicals
  Needed to get from room-sized to 1 cubic foot
  Costs rose from $15 million to $41 million

## Slide 14: Lander Instrumentation
Seismometer (only detected wind)
X-ray fluorescence spectrometer for composition of heavier elements in rocks and soils
  X-rays (from iron-55 and cadmium-109) bombard the soil, then each element produces its own characteristic x-rays, which are counted and recorded
Biological laboratory (3 different instruments)

## Slide 15: Biology Experiments in Soil
Contemporaneous Viking Documentary (5:28)

## Slide 16: Vikings’ Trip to Mars
Viking 1
  Launched August 20, 1975, on Titan / Centaur
  Course corrections August 27, 1975, and June 10 & 15, 1976
  Entered orbit June 19, 1976 (periapsis 1K mi, apoapsis 20K mi)
  Immediately found that the proposed landing site in Chryse Planitia (“Golden Plain”) was rougher than expected, and a new site on its western slope was chosen
  Successful landing July 20, 1976 (16 days late). Due to the speed-of-light time delay, touchdown on Earth was recorded 19 minutes after actual touchdown. The first pictures showed nearby rocks large enough to have prevented a safe landing.
Viking 2:
  Launched September 2, 1975
  Course correction September 19, 1975
  Entered orbit August 7, 1976
  Re-routed landing in Utopia Planitia
  Successful landing September 3, 1976, tilted 8.5◦

## Slide 17: Vikings 1 Launch (NY Times, p. 40)

## Slide 18: Vikings 1 Landing

## Slide 19: First Viking Photographs

## Slide 20: Viking Lander Results
Rated for 30 days, Viking 1 lander operated for 6 (Earth) years
Viking 2 lander operated for 3 ½ years
Sky was pinkish rather than blue, due to dust in the air
Winds were measured at 0 to 22 mph, temperatures from -122 to -22 Fahrenheit, pressures from 7 to 8 mbar with a 5% drop as CO2 froze onto the ice caps
The 6-foot robotic arm scooped up soil and deposited it in the chemistry lab
  X-ray fluorescence spectrometry showed primarily silicon and iron, with higher-than-expected sulfur
  Biology tests
    Results were positive, but generally concluded to be due to chemical oxidants produced by the effect of UV light on the soils
    Two original scientists and some recent work dissent
  GCMS showed no detectable organic chemicals except chlorinated compounds thought to be cleaning contaminants

## Slide 21: Viking Orbiter Results
Orbiters ran out of attitude control gas at 5 and 3 years respectively
North polar ice cap is water ice, not CO2 (dry ice)
Permafrost (subsurface ice) is prevalent
Moons appear similar in composition to asteroids
Thousands of pictures were taken

## Slide 22: Viking Photo of Drainage

## Slide 23: Viking Composite Picture
Valles Marineris

## Slide 24: Viking 1 and 2 Summary
Technical wins with first successful EDL and miniaturized GCMS
Clear evidence of past liquid water along with current conditions without liquid water stimulated research in global climate change
Negative biologic results reduced interest in Mars for several years
25th Anniversary (1:42) [original Viking team aged 25 years]

## Slide 25: Two Failures: Phobos and Mars Observer
Soviet Phobos 1 and 2 orbiters with landers (1988)
  Cooperation of 14 nations including US Deep Space Network
  Phobos 1 failed en-route: a single character error in an uploaded program resulted in turning off attitude control, and the batteries ran down
  Phobos 2 entered orbit around Mars and took 37 images of Phobos, but failed before the lander could be de-orbited
US Mars Observer (1992)
  $813 million orbiter designed to study elemental and mineralogical composition of the surface, gravitational and magnetic fields, temporal and spatial distribution of volatiles and dust, and circulation of the atmosphere
  Contact was lost 3 days before planned orbital insertion
  Likely cause was fuel and oxidizer leakage through a check valve during cruise resulting in an explosion when the engine was restarted for course correction

## Slide 26: Digression: Allan Hills 84001
Meteorite fragment found in Allan Hills Antarctica in 1984
Consensus Scientific Results
  Crystalized 4 billion years ago on Mars
  Blasted off Mars by a meteorite 17 million years ago
  Landed on Earth 13,000 years ago
Claims from McKay, et al. in Science, August 1996
  Bacteria-like structures found by scanning EM
  20-100 nm in diameter (smallest Earth bacteria are 200-300 nm)
  Used to bolster interest in detecting life on Mars
Current consensus is that these may be abiotic, and that morphology alone is too subjective to be used to declare life

## Slide 27: Three Mars missions launched in late 1996
Russia’s Mars 96
  Orbiter with 26 instruments built by multiple countries
  Two penetrators with 9 instruments each to measure ~15 feet into the surface
  Two landers with 8 instruments each
  Successfully placed in Earth parking orbit
  Failed ignition of rocket to leave Earth orbit
  Probably fell over Chile with 200 gm of plutonium-238, never recovered
US Mars Global Surveyor
  Launch November 1996
  Entered Mars orbit September 12, 1997
  Long orbital adjustment period via aerobraking
  Mapping began March 1999
  Operated until November 2006
US Pathfinder lander with Sojourner rover
  Launch December 1996
  Landing July 4, 1997
  Operated until September 27, 1997

## Slide 28: Mars Global Surveyor
Mapping mission designed to scout out landing sites
240,000 pictures at about ¼ mile resolution
First use of laser altimeter in space
Also measured temperature and magnetic fields
Polar orbit allowed essentially 100% coverage of the surface
Blue = low
Red and
Grey = high

## Slide 29: Pathfinder and Sojourner (Truth)
Follow-up to 1975-1976 Viking landers
Part of the post-Cold-War “cheaper, faster, better” Discovery Program of NASA administrator Dan Goldin
Project manager: Tony Spear
20th Anniversary: Initial idea (1:56) [Charles Elachi of JPL]
$150 million lander and $25 million rover
20th Anniversary: Development overview (6:31) [Brian Muirhead of JPL]
Landed July 4, 1996, on a plain 2.4 km below the average planetary surface altitude called Chryse Planitia in the north equatorial region
20th Anniversary: Control Room with artist renderings of the landing (5:35)

## Slide 30: Pathfinder Lander
3 feet tall, 1973 pounds at launch, 793 pounds at landing
IBM computer at 20 megaflops with 128 megabytes RAM
Stereo CCD cameras
with 12 color filters,
256x256 pixels
Weather station
Radios

## Slide 31: Sojourner (Truth) Rover
Named by the 12-year-old winner of a student competition to submit an essay about the historical accomplishments of a heroine
25 pounds, solar panels and a non-rechargeable battery, front and back cameras, radio, alpha proton x-ray spectrometer
Warm electronics box, rocker bogie with 6 independently actuated wheels, front and rear steering, obstacle avoidance, 1.5 ft/sec

## Slide 32: Sojourner (Truth) Rover: Instrumentation
APXS: Curium 244 (half life 18 years) emits alpha particles and measures alpha particles, protons, and x-rays scattered or emitted to determine elemental composition in the first few tens of µm of soil
Mounted on an actuator with contact sensors
Each measurement takes tens of hours

## Slide 33: Rover and Donna Shirley
Donna Shirley was a pilot and an aerospace engineer who worked at JPL on heat shields, rovers and robotics
Shirley was manager of the Mars Exploration Program at JPL, a key advocate of the rover, and the first woman Program Manager at NASA
NBC News (4:00) [A few garbled seconds]
Donna Shirley Hall of Fame: Sojourner (4:01)

## Slide 34: Pathfinder and Sojourner Science Results
Proved the workability of airbags for EDL
Lander returned 16,500 images
Pioneered Mars rover technology: 550 pictures, 40 feet from the lander, 330 feet total, collected APXS data at 16 locations
Lander provided extensive weather data including evidence of frequent dust devils and early morning water ice clouds
Found rounded rocks thought to be evidence of a time of flowing water
Found high silica content in rocks, different from the few Martian meteorites found on Earth
Soil chemistry was similar to Viking 1 and Viking 2, suggested planet wide circulation of soil and dust
Radio tracking of Pathfinder and its rotation was used to determine that the planetary core is 800 to 1250 miles in radius
Airborne dust was found to contain a magnetic form of iron oxide about 3 µm in diameter

## Slide 35: Winter 1998/1999 Launches
US Mars Climate Orbiter ($327 million)
  Designed to study atmosphere, climate and surface and do radio relay
  Failed at Mars orbit insertion due to Lockheed Martin’s failure to convert English to metric units
US Mars Polar Lander ($165 million)
  Designed to study soil and climate at the south pole
  “The Failure Review Board concluded that the most likely cause of the mishap was a software error that incorrectly identified vibrations, caused by the deployment of the stowed legs, as surface touchdown. The resulting action by the spacecraft was the shutdown of the descent engines, while still likely 40 meters above the surface.”
Japanese Nozomi (“Hope”)
  Designed to study Mars’ atmosphere and its interaction with the solar wind
  Designed to use moon and Earth swingbys to reduce fuel expenditure
  Valve failure during the Earth swingby left insufficient fuel
  Mission changed to heliocentric orbit with Mars flyby in December 2003
  Did provide data about deep space

## Slide 36: Summary of Week 2
Russia continues to fail in the 1990s, joined by Japan
US has a mix of successes and dramatic failures under NASA administrator Dan Goldin’s “faster, better, cheaper” approach

## Slide 37: What’s next
  Early 2000s: Odyssey, Spirit & Opportunity, Mars Express
  Late 2000s: Mars Reconnaissance Orbiter, Phoenix lander

## Slide 38: Pre-Viking Soviet Missions
Mars 4 to Mars 7 were intended for 1973 launch to pre-empt the 1976 US Viking mission, but planetary positioning was poor necessitating smaller payloads in the form of separate orbiter and lander launches.
A high failure rate of transistors made with aluminum rather than gold contacts predicted a 50% failure rate, but the missions were continued
Mars 4 lander could not do course correction to due transistor failure but sent back 12 pictures at 1200 miles.

## Slide 39: Pre-Viking Soviet Missions
Mars 5 orbiter successfully performed course corrections and entered Martian orbit February 2, 1974
A leak of the pressurized instrument compartment was detected, probably due to a micrometeroid, and only three weeks of operation was predicted. This meant the landers would have no orbiting relays.
An accelerated program of photography and scientific instrument observation was devised
Chemical composition of rocks was measured for the first time

## Slide 40: Pre-Viking Soviet Missions
Mars 6 was a lander with a flyby component
Multiple problems developed, one by one, with partial recovery by backup systems
Lander data rates were greatly reduced due the need for direct communication with Earth
The lander detached and decelerated, and the parachutes deployed but with evidence of instability
The first direct measurements of the Martian atmosphere were made: temperature and pressure and about 1/3 argon as measured by mass spectrometry (real value 1.6%)
Landing engines ignited, but no further data was received
Possible explanations include failure of the radio system or landing on large rocks
The Mars 7 lander failed to fire retro rockets and did not enter the Martian atmosphere

## Slide 41: Viking Rockets and Guidance
Titan III-Centaur
Solid booster rockets (polybutadiene acrylonitrile) assist main hydrazine/dinitrogen tetroxide engines
Hydrazine/dinitrogen-tetroxide second stage
Liquid hydrogen / liquid oxygen third launch stage
Hydrazine/dinitrogen-tetroxide engine on the spacecraft, plus compressed nitrogen attitude control jets
Course corrections based on Deep Space Network observations on Earth

## Slide 42: Entry, Descent and Landing
Biggest unknown: atmosphere too thin for Earth-like landing and too thick for Moon-like landing
Deorbit burn
Enters the atmosphere of Mars about 100 miles above the surface, traveling at about 18,000 miles per hour
Seven minutes later, it has to be traveling at one or two miles an hour to make a soft landing
Aeroshell braking until 3.7 miles and 600 mph
Supersonic parachute until about 5000 feet (by radar) when backshell separation occurs
Throttleable rockets slow to 1.5 mph
Shock absorbing legs
All with no Earth intervention (40-minute round trip communication delay)

## Slide 43: Biology Experiments in Soil
Gas Exchange
  Looked for a change in oxygen, CO2, nitrogen, hydrogen, or methane after adding nutrients or nutrients plus water
Labeled Release
  Added radioactive 14C labeled nutrients, then looked for 14C labeled gasses in the air above the soil
  Subsequently the samples were heated to 160 ℃ and retested as a control
Pyrolytic release
  Looking for carbon fixation through photosynthesis, 14C carbon dioxide and carbon monoxide were incubated with the soil for several days, then release of radioactivity from the soil was observed as it was heated

## Slide 44: Engineering Management
from Thomas A. Mutch and Kenneth L. Jones in “The Martian Landscape” (https://history.nasa.gov/SP-425/contents.htm)
Described about 400 meetings over 8 years in four locations:
“Useful exchanges of information prevented isolated journeys up blind alleys. When no obvious solution to a problem was apparent, we proceeded by vote. The majority opinion dictated the next step. In one sense, that appears absurd. Certain things are matters of fact. To what useful end can one vote on the proposition that a camera should cost no more than X dollars, whereas a biology instrument should cost Y dollars? Or that the average Martian atmospheric pressure is 1 percent of the Earth's atmosphere as opposed to 0.5 percent? Viewed in another context, an open meeting in which all participants have equal vote has served Americans well in many previous situations. Perhaps more than we realize, it is a method of pooling information with which we have grown up. I like to think that the ultimate success of Viking can be traced back to those countless meetings at which we chewed on one problem after another- hours of thoughtful criticism and, sometimes, clamorous sharp-edged debate.”