## Slide 1: Neonatal Ferret Visual System
Abby Fijas
Gary Klein
May 2, 2007

## Slide 2: Collaborative Project:
Bill Eddy, Dept. of Statistics, CMU
Justin Crowley, Dept. of Biology, CMU

## Slide 3: Ultimate Plan:
This study looks at the growth of neurons in the visual cortex.
Scientists also hope to understand why the optic nerve switches sides in the brain.
By lining up images taken at different times, neuron growth can be documented.
Problem: movement of the brain causes pixel movement in the images.

## Slide 4: What causes the movement?
This experiment is performed on neonatal ferrets. The reason for using ferrets is that they are born blind; allowing for the entire growth of neurons in the visual cortex to be observed.
Because images must be taken over time, the ferrets are in vivo, and thus the increase of blood flow from the heartbeat and respiration, although slow, cause the brain to move, thereby causing the pixels in the image to move.

## Slide 6: Project Goal:
The goal has always been to find a way to move the pixels back to their correct location in an image, to create what would be the “true” image. Now, we just have a different approach to doing this than we did before.
  Old Approach: Find a way to move each individual pixel to its ‘correct’ location in an image.
  New Approach: Create a correct image by taking the lines in the slices least effected by the physiological data and putting them together.

## Slide 7: Data Overview:
Notes: Talk about LSM here, which picks up the fluorescence of the GFP.

## Slide 8: Lining things Up:
In order to work with movement, we need to line up the two data sets, i.e. match their dimensions.
Luckily, the physiological data contains a synch channel that tells us when the microscope is scanning.

## Slide 9: Working with the Synch Channel:
Initially, after some exploratory analysis of the synch data, we thought that there were roughly 3 samples of physiological data for every line scan. That means that for each slice of an image there should be 512 triplicates of samples corresponding to times when the laser was scanning.

## Slide 10: Working with the Synch Channel:
Under this assumption, we worked to try and match up the dimensions of the two data sets.
The idea was to take the mean of each set of triplicates, and assign that value to every pixel of a line, doing this for all 512 lines in all z slices.
Notes: Explanation of why taking the mean was reasonable.

## Slide 11: Working with the Synch Channel:
After much coding first in Matlab and then in FIASCO, we discovered a problem.
Occasionally, the physiological data, skips some samples.
Notes: The skipping kept us from being able to match up the dimensions because we were occasionally missing some physiological data to match up with a line. Example for Mouse 5228, 8 of the 96 slices are missing one triplet.

## Slide 12: Solution:
Possible Cases:
  The missing points occur in the middle of scanning an image.
    Interpolate values from samples immediately after it.
  The missing points occurs at the beginning of scanning an image
    Add points to the beginning of the slice by using the points immediately following.
  The missing points occur at the very end of scanning an image.
    Append the missing points onto the end of the slice from those immediately before it.
Notes: Talk about frame synch

## Slide 13: New Plans:
Idea behind creating the “true image”:
Since we have multiple replications of x-y slices for each image, we can take the replication of each line associated with the minimum physiological effect (least movement) for that slice and put it in the new slice.

## Slide 14: Use of the Pulse Oximeter:

## Slide 15: What needed to be changed:
Dan Smith of the Biology Department started a system known as Brain Morey which is used to trigger the start of image acquisition based on where the ferret is in its QRS cycle.
Typically when imaging, three replications are taken, all beginning at the peak of they QRS cycle.
To make our idea work for the true image, we asked Dan to change the data acquisition to have lagged triggering. Thus, take multiple replications all beginning at different points in the QRS cycle.
By doing this, we are more or less guaranteed to find a minimum.
Notes: QRS cycle: all events having to do with the beginning of one heartbeat to the beginning of the next.
They typically start the trigger at the top of a beat.

## Slide 16: What needed to be changed:

## Slide 17: Future Plans/Ideas:
Create the true image.
  Need to complete some coding.
  Being able to create these new images should allow them to easily be lined up when trying to compare ones taken at different times.
Lagged triggering off of the QRS and respiration cycle.
Look at the signal to noise ratio.
  Problems based on new data acquisition.
  Solutions?